## Slide 1
SolarEye Security System
Alex Allahar, Zayan Prasla, Jackson Kitchel, Victor Igbokwe
Wonhyeok Jang
Figure 1. System Diagram
System Overiew
The SolarEye Security System uses solar-powered lighting, smart surveillance, and mobile alerts for real-time, automated, and low-maintenance security, ensuring safer, smarter public spaces.
Power Distribution
The Power Distribution system draws from a 12-volt battery, the system employs a buck converter [see Figure 3(A)] to step down the voltage to 5 volts, ensuring stable and efficient power delivery. This regulated 5-volt supply is essential for operating key components, including the charging ports and the Raspberry Pi. To enhance functionality, the LED lights are integrated through a dedicated PCB [see Figure 3(B)], which allows the Raspberry Pi to precisely control their operation. This setup enables seamless coordination between power distribution and system control, optimizing performance and efficiency.
A: Buck Converter PCB – Efficiently steps down 12V to a stable 5V supply.
B: Boost Converter PCB – Enables voltage regulation and control via the Raspberry Pi.
SolarEye App
The SolarEye App interfaces with the SolarEye Security System via Firebase, allowing comprehensive control over the system's camera and LED deterrence features. The home page provides an overview of Event History and Charging Statistics for the Solar Panel and Battery. In the Event History section, all recorded events are listed, complete with timestamps and event types. To ensure maximum security, the app's backend is fortified with email verification, two-step authentication, and SMS verification.
Figure 3. View of Printed Circuit Boards
Figure 6. Solar Power Charging Circuit Efficiency vs Output Voltage (Taken from MPPT Spec Sheet)
Figure 7. SolarEye App Home Page
Figure 2: Livestream Layout
Solar Generation
The Solar power generation subsystem serves as the central power source within our project. The subsystem is responsible for the solar panel, charging circuit PCB and supplying power to the 12-volt battery. The 100W solar panel is connected directly to the charging circuit PCB which regulates the power and supplies the 12-volt battery with a safe and efficient supply voltage. Additionally, the voltage and current supply from the solar panel as well as the battery are monitored by the charging circuit. These data points are then output by the PCB to be read and processed by the Raspberry Pi 4B. The main components of the schematic below are as follows:
A: BQ24650, which serves as the Maximum Power Point Tracking (MPPT) aspect of the circuit
B: ACS723 current sensor IC chips, placed at the input and output of the circuit
Figure 4.Simulation Results for the Buck Converter
Security
The SolarEye Security System has two modes: Passive Security and Active Surveillance. In Passive Mode, a PIR sensor triggers automated video capture, event logging, and Firebase storage. In Active Mode, users enable real-time streaming with OpenCV motion detection, sending alerts to Firebase for immediate response. This ensures efficient, continuous monitoring with optimized power use.
Figure 5. Solar Power Charging Circuit Schematic
Figure 8. SolarEye App Event History Page
Notes: Fix Overview diagram